## Slide 1: Distributing Collaborative Multi-Robot Planning with Gaussian Belief Propagation
Aalok Patwardhan, Riku Murai, Andrew J. Davison
IEEE Robotics and Automation Letters vol. 8, no. 2, pp. 552-559, Feb. 2023 doi: 10.1109/LRA.2022.3227858.

## Slide 2: Autonomous collaboration is the future
… but centralised motion planning is not scalable
https://cdn.motor1.com/images/mgl/1MW0K/s3/autonomous-vehicles-on-road-communicationg-with-wifi-signals-and-radar.jpg

## Slide 3: The GBP Planner (Gaussian Belief Propagation)
Robots can collaborate to plan safe and efficient paths with iterative message passing
Decentralised, via peer-to-peer communication
Asynchronous message passing brings robustness to communications failures
GBP Planner

## Slide 4: Path Planning: the optimisation of
Variables
Robot planned states (position and velocities)
Towards goals
t=1
t=2
t=K
Horizon state
Current state
t=0
under
Constraints
Dynamics
Obstacle avoidance
Inter-robot collision avoidance
(Nonlinear) cost functions
Factor Graph Inference

## Slide 5: Background: Gaussian Belief Propagation (GBP)
Decentralised and iterative inference on a factor graph
Node-wise local message passing to update beliefs of variables
Global factor graph distributed between many robots
https://gaussianbp.github.io/

## Slide 6
Dynamics factor
High cost if robot path is dynamically infeasible
Inter-robot factor
High cost if robot states overlap at same timestep
Current state
Robot A
t=0
Obstacle factor
High cost if state is near obstacles in environment
Current state
Robot B
Horizon state
t=0
t=1
t=2
t=K
Towards goals
t=1
t=2
t=K
Horizon state

## Slide 7
Dynamics factor
High cost if robot path is dynamically infeasible
Inter-robot factor
High cost if robot states overlap at same timestep
Current state
Robot A
t=0
Obstacle factor
High cost if state is near obstacles in environment
Current state
Robot B
Horizon state
t=0
t=1
t=2
t=K
Towards goals
t=1
t=2
t=K
Horizon state

## Slide 8
Dynamics factor
High cost if robot path is dynamically infeasible
Inter-robot factor
High cost if robot states overlap at same timestep
Current state
Robot A
t=0
Obstacle factor
High cost if state is near obstacles in environment
t=K
Horizon state
t=0
Current state
Robot B
t=1
t=2
Towards goals
t=1
t=2
t=K
Horizon state

## Slide 9: Circle Crossing Experiment
Robots of various sizes must avoid obstacles and each other
Better performance and scalability than ORCA1, a popular distributed reactive planner
Communications failure:
Collision-free paths even when a high proportion of messages are dropped
[1] J. van den Berg, S. Guy, M. Lin, and D. Manocha. Reciprocal N-body collision avoidance. Proceedings of the International Symposium on Robotics Research (ISRR), 2009

## Slide 10: Warehouse Junction Experiment
Robots travel at high speeds through a junction
Collaboration in GBP planner allows high flowrate to be maintained
Blockages caused by reactive planner
100m
Target speed: 100 km/h

## Slide 11: The GBP Planner
Robots can collaborate to plan safe and efficient paths with iterative message passing
Decentralised, therefore scalable to large numbers of robots
Wide reaching benefits for self-driving cars, teams of robots working together
100m

## Slide 12: Distributing Collaborative Multi-Robot Planning with Gaussian Belief Propagation
Aalok Patwardhan, Riku Murai, Andrew J. Davison
IEEE Robotics and Automation Letters vol. 8, no. 2, pp. 552-559, Feb. 2023 doi: 10.1109/LRA.2022.3227858.

## Slide 13: Section title to go here

## Slide 14
Section title to go here

## Slide 15: Title
Point 1
Point 2

## Slide 16: “For quotes” or call out text

## Slide 17: “For quotes” or call out text

## Slide 18: Logo Variations